## Slide 1: Matlab Simulink & MiP
Kurt Talke
12/3/2018

## Slide 2: Outline
Matlab Simulink
MiP Demo
Getting started
  Matlab toolboxes
  BBB setup
  Simulink setup

## Slide 3: Simulink
Graphical model-based developmental tool
  https://www.mathworks.com/videos/simulink-overview-61216.html
Tutorial links/videos
  https://www.mathworks.com/videos/getting-started-with-simulink-69027.html
  https://www.mathworks.com/videos/getting-started-with-simulink-part-1-building-and-simulating-a-simple-simulink-model-1508442030520.html
What is happening under the hood:
  Mathworks support package interfaces with BBBlue.
  Low level c-code wrapped into S-Blocks to touch hardware on BBB
    Ex: rc_motor_set, rc_mpu_read_accel, rc_mpu_read_gyro, rc_encoder_read, etc…
  Interesting logic and controls done in Simulink

## Slide 4: MiP Demo
Demo Time
Balance Simulink model split into two parts:
  Logic – for smooth start/stop behavior
  Discrete time controller implementation
    Discrete time controller
    Plant

## Slide 5: Plant
Support package has S-Blocks to touch BBBlue hardware

## Slide 6: Discrete time controller implementation
Controller
Saturation
Plant

## Slide 7: Controller
2 separate filters with DT controllers

## Slide 8: Simulink
Need to install the following Matlab Toolboxes:
  Simulink
  Simulink coder
  Embedded coder
  Simulink embedded coder
  Beagle bone blue support package

## Slide 9: Getting Started: BBBlue
Install Debian 9.5 from 10/7/2018 (4.14.71)
  https://debian.beagleboard.org/images/
  Use “bone-debian-9.5-iot-armhf-2018-10-07-4gb.img.xz” to create a bootable SD card.
  Flash using etcher
ssh into BBBBlue after boot using wifi hotspot:
  $ ssh debian@192.168.7.2 (terminal for mac/linux, putty for Windows)
  debian@192.168.7.2's password: “temppwd”
Check:
  debian@beaglebone:~$ rc_version
  1.0.3
  debian@beaglebone:~$ uname -a
  Linux beaglebone 4.14.71-ti-r80 #1 SMP PREEMPT Fri Oct 5 23:50:11 UTC 2018 armv7l GNU/Linux

## Slide 10: Getting Started: Matlab
Get BBB-Blue support package
  New version to be released this week
  Support for RC version 1.0.3
FCCR IMU Driver
  https://github.com/ktalke12/Matlab_MiP
  Read the “ReadMe”

## Slide 11: Matlab Setup
Manage Add-Ons
Setup BBBlue
Click on Setup

## Slide 12: Matlab Setup
Follow setup instructions
  Can setup wifi on UCSD Protected network:
    PEAP, MSCHAPv2, username & password

## Slide 13: Getting Started: Simulink
Configuration Parameters:
  Set proper IP address in Balance.slx file
Set mode to “External”

## Slide 14: Conclusion
Very easy to get started using BBBlue support package
Balance in Simulink already designed
Can use test your controllers
More exciting development possible
  Steering control
  IMU interrupt implementation